HELLA LED industrial luminaire ALU (4 modules) with four independent 15W LED modules each with 8 LEDs. Connection rating 60W, 5,000 lumen, color temperature 4000°/5000° K. Incl. dimming to 50%, by switching off one phase (night-time reduction). Decline in luminous flux over a total operating period of 50,000 h not greater than 20%.

220V-240V AC, 50Hz /AC. Overvoltage protection 6 KV. Degree of protection IP 65 for high pressure cleaner as per DIN 4005, SK II, LED module with integrated electronic ballast and rotational optics made of PMMA can be changed in operation via a plug-in connection without additional tools. The distribution of the light from the luminaire can be varied by the arrangement of the modules. The housing is made of aluminum. The surface is powder coated. Luminaire wired ready to connect with polyurethane connection cable 3x1mm² without earth conductor, cable length 1m. Dimensions (LxWxH) 510x415x93 mm. Weight 12 kg.. Spare parts will be available for at least 20 years.

HELLA LED industrial luminaire ALU (4 modules) with four independent 21W LED modules each with 8 LEDs. Connection rating 84W, 6,800 lumen, color temperature 4000°/5000° K. Incl. dimming to 50%, by switching off one phase (night-time reduction). Decline in luminous flux over a total operating period of 50,000 h not greater than 20%.

220V-240V AC, 50Hz /AC. Overvoltage protection 6 KV. Degree of protection IP 65 for high pressure cleaner as per DIN 4005, SK II, LED module with integrated electronic ballast and rotational optics made of PMMA can be changed in operation via a plug-in connection without additional tools. The distribution of the light from the luminaire can be varied by the arrangement of the modules. The housing is made of aluminum. The surface is powder coated. Luminaire wired ready to connect with polyurethane connection cable 3x1mm² without earth conductor, cable length 1m. Dimensions (LxWxH) 510x415x93 mm. Weight 12 kg.. Spare parts will be available for at least 20 years.

HELLA LED industrial luminaire PLASTIC (4 modules) with four independent 15W LED modules each with 8 LEDs. Connection rating 60W, 5,000 lumen, color temperature 4000°/5000° K. Incl. dimming to 50%, by switching off one phase (night-time reduction). Decline in luminous flux over a total operating period of 50,000 h not greater than 20%.

220V-240V AC, 50-60Hz /AC. Overvoltage protection 6 KV. Degree of protection IP 65 for high pressure cleaner as per DIN 4005, SK II, LED module with integrated electronic ballast and rotational optics made of PMMA can be changed in operation via a plug-in connection without additional tools. The distribution of the light from the luminaire can be varied by the arrangement of the modules. The housing is made of PC. Fastening plate made of steel with surface protection. Luminaire wired ready to connect with polyurethane connection cable 3x1mm² without earth conductor, cable length 1m. Dimensions (LxWxH) 510x424x100 mm. Weight 7.8 kg.. Spare parts will be available for at least 20 years.

HELLA LED industrial luminaire PLASTIC (4 modules) with four independent 21W LED modules each with 8 LEDs. Connection rating 84W, 6,800 lumen, color temperature 4000°/5000° K. Incl. dimming to 50%, by switching off one phase (night-time reduction). Decline in luminous flux over a total operating period of 50,000 h not greater than 20%.

220V-240V AC, 50-60Hz /AC. Overvoltage protection 6 KV. Degree of protection IP 65 for high pressure cleaner as per DIN 4005, SK II, LED module with integrated electronic ballast and rotational optics made of PMMA can be changed in operation via a plug-in connection without additional tools. The distribution of the light from the luminaire can be varied by the arrangement of the modules. The housing is made of PC. Fastening plate made of steel with surface protection. Luminaire wired ready to connect with polyurethane connection cable 3x1mm² without earth conductor, cable length 1m. Dimensions (LxWxH) 510x424x100 mm. Weight 7.8 kg.. Spare parts will be available for at least 20 years.

HELLA LED industrial luminaire extruded aluminum profile (1 module) with one independent 15W LED module with 8 LEDs. Connection rating 15W, 1,250 lumen, color temperature 4000°/5000° K. Incl. dimming to 50%, by switching off one phase (night-time reduction). Decline in luminous flux over a total operating period of 50,000 h not greater than 20%.

220V-240V AC, 50Hz /AC. Overvoltage protection 6 KV. Module degree of protection IP 65 for high pressure cleaner as per DIN 4005, luminaire IP 54, SK II, LED module with integrated electronic ballast and optics made of PMMA can be changed in operation via a plug-in connection without additional tools. The distribution of the light from the luminaire can be varied by the arrangement of the modules. The housing comprises extruded aluminum profile (painted). Plastic components made of PC. Luminaire ready to connect without earth conductor.

Dimensions (LxWxH) 515x102x105 mm. Weight 2.6 kg.. Spare parts will be available for at least 20 years.

HELLA LED industrial luminaire extruded aluminum profile (1 module) with one independent 21W LED module with 8 LEDs. Connection rating 21W, 1,700 lumen, color temperature 4000°/5000° K. Incl. dimming to 50%, by switching off one phase (night-time reduction). Decline in luminous flux over a total operating period of 50,000 h not greater than 20%.

220V-240V AC, 50Hz /AC. Overvoltage protection 6 KV. Module degree of protection IP 65 for high pressure cleaner as per DIN 4005, luminaire IP 54, SK II, LED module with integrated electronic ballast and optics made of PMMA can be changed in operation via a plug-in connection without additional tools. The distribution of the light from the luminaire can be varied by the arrangement of the modules. The housing comprises extruded aluminum profile (painted). Plastic components made of PC. Luminaire ready to connect without earth conductor.

Dimensions (LxWxH) 515x102x105 mm. Weight 2.6 kg.. Spare parts will be available for at least 20 years.

HELLA LED industrial luminaire extruded aluminum profile (2 modules) with two independent 15W LED modules each with 8 LEDs. Connection rating 30W, 2,500 lumen, color temperature 4000°/5000° K. Incl. dimming to 50%, by switching off one phase (night-time reduction). Decline in luminous flux over a total operating period of 50,000 h not greater than 20%.

220V-240V AC, 50Hz /AC. Overvoltage protection 6 KV. Module degree of protection IP 65 for high pressure cleaner as per DIN 4005, luminaire IP 54, SK II, LED module with integrated electronic ballast and optics made of PMMA can be changed in operation via a plug-in connection without additional tools. The distribution of the light from the luminaire can be varied by the arrangement of the modules. The housing comprises extruded aluminum profile (painted). Plastic components made of PC. Luminaire ready to connect without earth conductor.

Dimensions (LxWxH) 1005x102x105 mm. Weight 5.2 kg.. Spare parts will be available for at least 20 years.

HELLA LED industrial luminaire extruded aluminum profile (2 modules) with two independent 21W LED modules each with 8 LEDs. Connection rating 42W, 3,400 lumen, color temperature 4000°/5000° K. Incl. dimming to 50%, by switching off one phase (night-time reduction). Decline in luminous flux over a total operating period of 50,000 h not greater than 20%.

220V-240V AC, 50Hz /AC. Overvoltage protection 6 KV. Module degree of protection IP 65 for high pressure cleaner as per DIN 4005, luminaire IP 54, SK II, LED module with integrated electronic ballast and optics made of PMMA can be changed in operation via a plug-in connection without additional tools. The distribution of the light from the luminaire can be varied by the arrangement of the modules. The housing comprises extruded aluminum profile (painted). Plastic components made of PC. Luminaire ready to connect without earth conductor.

Dimensions (LxWxH) 1005x102x105 mm. Weight 5.2 kg.. Spare parts will be available for at least 20 years.