Eco StreetLine Park 21W (top- and side-mounted post luminaire) with one independent 21W LED module with 8 LEDs. Connection rating 21W, 1700 lumen, color temperature 4000°/ 5000° K. Incl. dimming to 50%, by switching off one phase (night-time reduction). Decline in luminous flux over a total operating period of 50,000 h not greater than 20%.

220V-240V AC, 50Hz /AC. Overvoltage protection 6 KV. Degree of protection IP 67/ IP 69 for high pressure cleaner as per DIN 4005, SK II, LED module with integrated electronic ballast and free-form optics made of PMMA can be changed in operation via a plug-in connection without additional tools. The distribution of the light from the luminaire can be varied by the arrangement of the modules. The housing of the top-/side-mounted post luminaire is corrosion-resistant, it comprises die-cast aluminum with a low portion of copper. The surface is chromated and powder coated, similar to matt metallic light gray DB 703. Inclination can be adjusted in 5°-steps from  -15° to +15°. Luminaire wired ready to connect with polyurethane connection cable 3x1mm² without earth conductor, cable length 5-10m can be selected. Dimensions (LxWxH) 680x160x110 mm. Weight 6.5 kg. Spigot size 60/76mm. Spare parts will be available for at least 20 years.

Eco StreetLine Park 15W (top- and side-mounted post luminaire) with one independent 15W LED module with 8 LEDs. Connection rating 15W, 1250 lumen, color temperature 4000°/ 5000° K. Incl. dimming to 50%, by switching off one phase (night-time reduction). Decline in luminous flux over a total operating period of 50,000 h not greater than 20%.

110V-240V AC, 50Hz /AC. Overvoltage protection 6 KV. Degree of protection IP 67/ IP 69 for high pressure cleaner as per DIN 4005, SK II, LED module with integrated electronic ballast and free-form optics made of PMMA can be changed in operation via a plug-in connection without additional tools. The distribution of the light from the luminaire can be varied by the arrangement of the modules. The housing of the top-/side-mounted post luminaire is corrosion-resistant, it comprises die-cast aluminum with a low portion of copper. The surface is chromated and powder coated, similar to matt metallic light gray DB 703. Inclination can be adjusted in 5°-steps from  -15° to +15°. Luminaire wired ready to connect with polyurethane connection cable 3x1mm² without earth conductor, cable length 5-10m can be selected. Dimensions (LxWxH) 680x160x110 mm. Weight 6.5 kg. Spigot size 60/76mm. Spare parts will be available for at least 20 years.

Eco StreetLine Park 13W (top- and side-mounted post luminaire) with one independent 13W LED module with 8 LEDs. Connection rating 13W, 800 lumen, color temperature 4000°/ 5000° K. Incl. dimming to 50%, by switching off one phase (night-time reduction). Decline in luminous flux over a total operating period of 50,000 h not greater than 20%.

100V-240V AC, 50-60Hz /AC. Overvoltage protection 6 KV. Degree of protection IP 67/ IP 69 for high pressure cleaner as per DIN 4005, SK II, LED module with integrated electronic ballast and free-form optics made of PMMA can be changed in operation via a plug-in connection without additional tools. The distribution of the light from the luminaire can be varied by the arrangement of the modules. The housing of the top-/side-mounted post luminaire is corrosion-resistant, it comprises die-cast aluminum with a low portion of copper. The surface is chromated and powder coated, similar to matt metallic light gray DB 703. Inclination can be adjusted in 5°-steps from  -15° to +15°. Luminaire wired ready to connect with polyurethane connection cable 3x1mm² without earth conductor, cable length 5-10m can be selected. Dimensions (LxWxH) 680x160x110 mm. Weight 6.5 kg. Spigot size 60/76mm. Spare parts will be available for at least 20 years.

Eco StreetLine Park 10W (top- and side-mounted post luminaire) with one independent 10W LED module with 8 LEDs. Connection rating 10W, 620 lumen, color temperature 4000°/ 5000° K. Incl. dimming to 50%, by switching off one phase (night-time reduction). Decline in luminous flux over a total operating period of 50,000 h not greater than 20%.

100V-240V AC, 50-60Hz /AC. Overvoltage protection 6 KV. Degree of protection IP 67/ IP 69 for high pressure cleaner as per DIN 4005, SK II, LED module with integrated electronic ballast and free-form optics made of PMMA can be changed in operation via a plug-in connection without additional tools. The distribution of the light from the luminaire can be varied by the arrangement of the modules. The housing of the top-/side-mounted post luminaire is corrosion-resistant, it comprises die-cast aluminum with a low portion of copper. The surface is chromated and powder coated, similar to matt metallic light gray DB 703. Inclination can be adjusted in 5°-steps from  -15° to +15°. Luminaire wired ready to connect with polyurethane connection cable 3x1mm² without earth conductor, cable length 5-10m can be selected. Dimensions (LxWxH) 680x160x110 mm. Weight 6.5 kg. Spigot size 60/76mm. Spare parts will be available for at least 20 years.

Eco StreetLine Park 6W (top- and side-mounted post luminaire) with one independent 6W LED module with 8 LEDs. Connection rating 6W, 380 lumen, color temperature 4000°/ 5000° K. Incl. dimming to 50%, by switching off one phase (night-time reduction). Decline in luminous flux over a total operating period of 50,000 h not greater than 20%.

100V-240V AC, 50-60Hz /AC. Overvoltage protection 6 KV. Degree of protection IP 67/ IP 69 for high pressure cleaner as per DIN 4005, SK II, LED module with integrated electronic ballast and free-form optics made of PMMA can be changed in operation via a plug-in connection without additional tools. The distribution of the light from the luminaire can be varied by the arrangement of the modules. The housing of the top-/side-mounted post luminaire is corrosion-resistant, it comprises die-cast aluminum with a low portion of copper. The surface is chromated and powder coated, similar to matt metallic light gray DB 703. Inclination can be adjusted in 5°-steps from  -15° to +15°. Luminaire wired ready to connect with polyurethane connection cable 3x1mm² without earth conductor, cable length 5-10m can be selected. Dimensions (LxWxH) 680x160x110 mm. Weight 6.5 kg. Spigot size 60/76mm. Spare parts will be available for at least 20 years.