Eco StreetLine Twin 42W (top- and side-mounted post luminaire) with two independent 21W LED modules each with 8 LEDs. Connection rating 42W, 3,400 lumen, color temperature 4,000°/ 5,000° K. Incl. dimming to 50%, by switching off one phase (night-time reduction). Decline in luminous flux over a total operating period of 50,000 h not greater than 20%.

220V-240V AC, 50Hz /AC. Overvoltage protection 6 KV. Degree of protection IP 67/ IP 69 for high pressure cleaner as per DIN 4005, SK II, LED module with integrated electronic ballast and free-form optics made of PMMA can be changed in operation via a plug-in connection without additional tools. The distribution of the light from the luminaire can be varied by the arrangement of the modules. The housing of the top-/side-mounted post luminaire is corrosion-resistant, it comprises die-cast aluminum with a low portion of copper. The surface is chromated and powder coated, similar to matt metallic light gray DB 703. Inclination can be adjusted in 5°-steps from  -15° to +15°. Luminaire wired ready to connect with polyurethane connection cable 3x1mm² without earth conductor, cable length 5-10m can be selected. Dimensions (LxWxH) 680x220x110 mm. Weight 9.5 kg. Spigot size 60/76mm. Spare parts will be available for at least 20 years.

Eco StreetLine Twin 30W (top- and side-mounted post luminaire) with two independent 15W LED modules each with 8 LEDs. Connection rating 30W, 2500 lumen, color temperature 4000°/ 5000° K. Incl. dimming to 50%, by switching off one phase (night-time reduction). Decline in luminous flux over a total operating period of 50,000 h not greater than 20%.

220V-240V AC, 50Hz /AC. Overvoltage protection 6 KV. Degree of protection IP 67/ IP 69 for high pressure cleaner as per DIN 4005, SK II, LED module with integrated electronic ballast and free-form optics made of PMMA can be changed in operation via a plug-in connection without additional tools. The distribution of the light from the luminaire can be varied by the arrangement of the modules. The housing of the top-/side-mounted post luminaire is corrosion-resistant, it comprises die-cast aluminum with a low portion of copper. The surface is chromated and powder coated, similar to matt metallic light gray DB 703. Inclination can be adjusted in 5°-steps from  -15° to +15°. Luminaire wired ready to connect with polyurethane connection cable 3x1mm² without earth conductor, cable length 5-10m can be selected. Dimensions (LxWxH) 680x220x110 mm. Weight 9.5 kg. Spigot size 60/76mm. Spare parts will be available for at least 20 years.

Eco StreetLine Twin 26W (top- and side-mounted post luminaire) with two independent 13W LED modules each with 8 LEDs. Connection rating 26W, 1600 lumen, color temperature 4000°/ 5000° K. Incl. dimming to 50%, by switching off one phase (night-time reduction). Decline in luminous flux over a total operating period of 50,000 h not greater than 20%.

100V-240V AC, 50-60Hz /AC. Overvoltage protection 6 KV. Degree of protection IP 67/ IP 69 for high pressure cleaner as per DIN 4005, SK II, LED module with integrated electronic ballast and free-form optics made of PMMA can be changed in operation via a plug-in connection without additional tools. The distribution of the light from the luminaire can be varied by the arrangement of the modules. The housing of the top-/side-mounted post luminaire is corrosion-resistant, it comprises die-cast aluminum with a low portion of copper. The surface is chromated and powder coated, similar to matt metallic light gray DB 703. Inclination can be adjusted in 5°-steps from  -15° to +15°. Luminaire wired ready to connect with polyurethane connection cable 3x1mm² without earth conductor, cable length 5-10m can be selected. Dimensions (LxWxH) 680x220x110 mm. Weight 9.5 kg. Spigot size 60/76mm. Spare parts will be available for at least 20 years.

Eco StreetLine Twin 20W (top- and side-mounted post luminaire) with two independent 10W LED modules each with 8 LEDs. Connection rating 20W, 1240 lumen, color temperature 4000°/ 5000° K. Incl. dimming to 50%, by switching off one phase (night-time reduction). Decline in luminous flux over a total operating period of 50,000 h not greater than 20%.

100V-240V AC, 50-60Hz /AC. Overvoltage protection 6 KV. Degree of protection IP 67/ IP 69 for high pressure cleaner as per DIN 4005, SK II, LED module with integrated electronic ballast and free-form optics made of PMMA can be changed in operation via a plug-in connection without additional tools. The distribution of the light from the luminaire can be varied by the arrangement of the modules. The housing of the top-/side-mounted post luminaire is corrosion-resistant, it comprises die-cast aluminum with a low portion of copper. The surface is chromated and powder coated, similar to matt metallic light gray DB 703. Inclination can be adjusted in 5°-steps from  -15° to +15°. Luminaire wired ready to connect with polyurethane connection cable 3x1mm² without earth conductor, cable length 5-10m can be selected. Dimensions (LxWxH) 680x220x110 mm. Weight 9.5 kg. Spigot size 60/76mm. Spare parts will be available for at least 20 years.

Eco StreetLine Twin 12W (top- and side-mounted post luminaire) with two independent 6W LED modules each with 8 LEDs. Connection rating 12W, 760 lumen, color temperature 4000°/ 5000° K. Incl. dimming to 50%, by switching off one phase (night-time reduction). Decline in luminous flux over a total operating period of 50,000 h not greater than 20%.

100V-240V AC, 50-60Hz /AC. Overvoltage protection 6 KV. Degree of protection IP 67/ IP 69 for high pressure cleaner as per DIN 4005, SK II, LED module with integrated electronic ballast and free-form optics made of PMMA can be changed in operation via a plug-in connection without additional tools. The distribution of the light from the luminaire can be varied by the arrangement of the modules. The housing of the top-/side-mounted post luminaire is corrosion-resistant, it comprises die-cast aluminum with a low portion of copper. The surface is chromated and powder coated, similar to matt metallic light gray DB 703. Inclination can be adjusted in 5°-steps from  -15° to +15°. Luminaire wired ready to connect with polyurethane connection cable 3x1mm² without earth conductor, cable length 5-10m can be selected. Dimensions (LxWxH) 680x220x110 mm. Weight 9.5 kg. Spigot size 60/76mm. Spare parts will be available for at least 20 years.